## Slide 1: RRT* Implementation
WAI NWE TUN
Autonomous Robotics

## Slide 2: Contents
RRT*
Implementation
Results
Limitations
References

## Slide 3: RRT*
RRT* starts with an empty tree and adds a single node corresponding to the initial state.
It finds solution to motion planning problem.

## Slide 4: Implementation
It is assumed that there is no obstacles.
Cost is determined by Euclidean distance.
Six main functions are created:
  getSample()
  findNearest()
  steering()
  isObstacleFree()
  getNeighbors()
  chooseParent()
  insertNode()
  reWire()

## Slide 5: Implementation
To run RRT*, eight inputs are necessary:
  Starting point
  Goal point
  Obstacle points
  Threshold value
  Maximum number of nodes
  Step size
  Neighborhood size
  Random generating seed
Output : total cost and time, locations of generated nodes

## Slide 6: Result
Nodes: 5000 => Cost 208, Time: 104 sec

## Slide 7: getSample()
function node = getSample()
x = 0;
y = 0;
a = 0;
b = 200;
node = [x;y];
node(1) = (b-a) * rand(1) + a;
node(2) = (b-a) * rand(1) + a; end
This is to get a random node within ranges of x and y axis.

## Slide 8: findNearest()
This is to find the nearest node from the randomly generated new node (getSample()).
function indx = findNearest(rrt, n)
mindist = norm(rrt{1}.p - n);
indx = 1;
for i = 2:length(rrt)
dist = norm(rrt{i}.p - n);
if (dist<mindist)
mindist = dist;
indx = i;
end
end
end

## Slide 9: steering()
This is to find a new node which must be on the line of the random node and the nearest node, within the specified step size.
function new_node=steering(nearest_node, random_node)
dist = norm(random_node-nearest_node);
ratio_distance = param.step_size/dist;
x = (1-ratio_distance).* nearest_node(1)+ratio_distance
.* random_node(1);
y = (1-ratio_distance).* nearest_node(2) +ratio_distance
.* random_node(2);
new_node = [x;y];
end

## Slide 10: isObstacleFree()
This is to check if an obstacle exists at the new steered point.
function free=isObstacleFree(node_free)
  free = 1;
  for i = 1: length(param.obstacles(:,1))
  obstacle = param.obstacles(i,:);
  op1 = [obstacle(1), obstacle(2)];
  op2 = [op1(1)+obstacle(3), op1(2)];
  op3 = [op2(1), op1(2) + obstacle(4)];
  op4 = [op1(1), op3(2)];
  nx = node_free(1);
  ny = node_free(2);
  if ((nx>=op1(1) && nx<=op2(1)) && (ny>=op1(2) && ny<=op4(2)))
  free = 0;
  end
  end
end

## Slide 11: getNeighbors()
This is to get a list of nodes within the specified neighborhood region.
function neighbors = getNeighbors(rrt, node)
neighbors = [];
for i = 1:length(rrt)
rrt{i}.p dist = norm(rrt{i}.p-node);
if (dist<=param.neighbourhood)
neighbors = [neighbors i];
end
end
end

## Slide 12: chooseParent()
This is to choose the parent node for the new child node with the lowest cost from the root node.
function parent = chooseParent(rrt, neighbors, nearest, new_node)
min_cost = getCostFromRoot(rrt, nearest, new_node);
parent = nearest;
for i=1:length(neighbors)
cost = getCostFromRoot(rrt, neighbors(i), new_node);
if (cost<min_cost)
min_cost = cost;
parent = neighbors(i);
end
end
end

## Slide 13: InsertNode()
This is to insert a node to the existing rrt tree.
function rrt = insertNode(rrt, parent, new_node)
node.p = new_node;
node.iPrev = parent;
node.cost = rrt{parent}.cost + norm(rrt{parent}.p-new_node);
rrt{end+1} = node;
end

## Slide 14: reWire()
This is to reconsider to reconnect with the new node and its neighbor nodes if the cost is cheaper.
function rrt = reWire(rrt, neighbors, parent, new)
for i=1:length(neighbors)
cost = rrt{new}.cost + norm(rrt{neighbors(i)}.p - rrt{new}.p);
if (cost<rrt{neighbors(i)}.cost)
rrt{neighbors(i)}.iPrev = new;
end
end
end

## Slide 15: Result
Generating two new nodes

## Slide 16: Result
Threshold = 3, Step size : 5, Nodes: 1000 => Cost: 205, Time: 6 sec

## Slide 17: Result
Nodes: 2000 => Cost: 210, Time: 18 sec

## Slide 18: Result
Nodes: 5000 => Cost 208, Time: 104 sec

## Slide 19: Result
Nodes: 8000 => Cost 206, Time: 256 sec

## Slide 20: Limitations
Obstacle must be rectangle-shaped.
Obstacle can be detected only at the end points. Thus, if the end points is obstacle-free, it is considered as valid point even if line between the points passed through the obstacle.
Neighborhood size must be equal to step size.
  No steering need not be performed in rewiring.
It is only available for 2D path planning problem.

## Slide 21: References
S. Karaman, et. al., ‘Anytime Motion Planning using the RRT*,’ IEEE on Robotics and Automation, May 2011.
https://math.stackexchange.com/questions/175896/finding-a-point-along-a-line-a-certain-distance-away-from-another-point
https://github.com/vivekprayakarao
https://www.youtube.com/watch?v=JM7kmWE8Gtc&t=205s